## Slide 1: Mycobot Software Installation and Usage
2023.6.04

## Slide 2: Installation
Preapre a ROS PC
  Install Ubuntu 20.04 64bit
  Install ROS Foxy follow this url: https://docs.ros.org/en/foxy/Installation.html
And then, please install following dependencies:
  sudo apt install python3-rosdep
  sudo apt install python3-rosdep2
  sudo rosdep init
  rosdep update
  sudo apt update
  sudo apt install rospack-tools
  sudo apt install python3-colcon-common-extensions
  sudo apt install python3-colcon-mixin
  colcon mixin add default https://raw.githubusercontent.com/colcon/colcon-mixin-repository/master/index.yaml
  colcon mixin update default
  sudo apt install python3-vcstool
  sudo apt install -y ros-foxy-xacro ros-foxy-moveit ros-foxy-moveit-servo ros-foxy-ros2-control ros-foxy-ros2-controllers ros-foxy-moveit-ros-move-group ros-foxy-moveit-planners-ompl ros-foxy-moveit-kinematics ros-foxy-gazebo-ros ros-foxy-gazebo-ros2-control ros-foxy-controller-manager ros-foxy-joint-state-broadcaster ros-foxy-joint-state-publisher-gui ros-foxy-joint-trajectory-controller ros-foxy-moveit-ros-perception ros-foxy-rviz-visual-tools ros-foxy-moveit-resources

## Slide 3: Installation
Switch to Cyclone DDS
sudo apt install ros-foxy-rmw-cyclonedds-cpp
Add this line to ~/.bashrc to source it automatically
export RMW_IMPLEMENTATION=rmw_cyclonedds_cpp

## Slide 4: Setup
Connect Mycobot and ROS PC to same network layer.
Run following command on Mycobot
  source /opt/ros/galactic/setup.bash
  export ROS_DOMAIN_ID=30
Run following command on ROS PC
  export ROS_DOMAIN_ID=30

## Slide 5: Setup Mycobot
Copy control_node.py in mycobot_280pi_utils folder
to /mycobot_ros2/mycobot_280/mycobot_280pi/mycobot_280pi.
Add 'control_node = mycobot_280pi.control_node:main’
to mycobot_ros2/mycobot_280/mycobot_280pi/setup.py.
Run control_node on Mycobot.
ros2 run mycobot_280pi control_node --ros-args -p robot:=robot0
If there are 2 Mycobot, change the robot0 to robot1 on the second robot.

## Slide 6: Setup Sigma on ROS PC
Using following commands to setup Sigma
  wget https://www.forcedimension.com/downloads/sdk/sdk-3.15.0-linux-x86_64-gcc.tar.gz
  tar -xzvf sdk-3.15.0-linux-x86_64-gcc.tar.gz
check ld -ldhd --verbos / ld -ldrd –verbos
copy libdhd.a, libdrd.a to library folder
  sudo mkdir -p /usr/local/lib/x86_64-linux-gnu
  cd /sdk-3.15.0/lib/release/lin-x86_64-gcc
  sudo cp libdhd.a /usr/local/lib/x86_64-linux-gnu/libdhd.a
  sudo cp libdrd.a /usr/local/lib/x86_64-linux-gnu/libdrd.a

## Slide 7: Usage
To use one Sigma with one Mycobot
**On Mycobot** ros2 run mycobot_280pi control_node --ros-args -p robot:=robot0
**On ROS PC (connect Sigma)**
Run Sigma node
ros2 launch sigma sigma.launch.py
Run Sigma and Mycobot bridge node
ros2 launch mycobot_280pi one_sigma_mycobot.launch.py robot_name:=robot0 sigma_name:=sigma0

## Slide 8: Usage
To use two Sigma with two Mycobot
**On Mycobot_0**
ros2 run mycobot_280pi control_node --ros-args -p robot:=robot0
``` **On Mycobot_1**
ros2 run mycobot_280pi control_node --ros-args -p robot:=robot1
``` **On ROS PC**
ros2 launch sigma sigma.launch.py
ros2 launch mycobot_280pi two_sigma_mycobot.launch.py robot0_name:=robot0 sigma0_name:=sigma0 robot1_name:=robot1 sigma1_name:=sigma1
```

## Slide 9: Usage
To use one Mycobot with Moveit **On Mycobot**
ros2 run mycobot_280pi control_node --ros-args -p robot:=robot0
**On ROS PC**
Run moveit launch (this default robot name is robot0)
ros2 launch mycobot_280pi_moveit mycobot_280pi_moveit_launch.py

## Slide 10: Usage
To use two Mycobot with Moveit
**On Mycobot_0**
ros2 run mycobot_280pi control_node --ros-args -p robot:=robot0
``` **On Mycobot_1**
ros2 run mycobot_280pi control_node --ros-args -p robot:=robot1
``` **On ROS PC** Run moveit launch (this default robot name is robot0 and robot1 init pos is 0 0 0 and 0 0.5 0)
ros2 launch mycobot_280pi_moveit two_mycobot_280pi_moveit_launch.py
Currently the default name of robot (robot0 and robot1 cannot be change, change xyz, rpy to modify robot position.
robot0_name:=robot0 robot0_xyz:='"0 0 0"' robot0_rpy:='"0 0 0"' robot1_name:=robot1 robot1_xyz:='"0 0.5 0"' robot1_rpy:='"0 0 0"'
```

## Slide 11: Usage
Motion Record
To use motion record, please start following cmd
ros2 run mycobot_280pi mycobot_motion_record.py --ros-args -p robot:=robot0
If use 2 robots, please run on 2 terminals and start the second node with robot:=robot1

## Slide 12: Usage
Other Use
Config To set the workspace for robot, please modify the **workspace_params.yaml** in **mycobot_280pi/config** and rebuild the software.
Dummy robot This pakage provide dummy robot.
The robot can be controlled by /control_radians topic. The **quantity:=1** is number of robot. The robot name will start from 0.
ros2 launch mycobot_280pi mycobot_dummies.launch.py quantity:=1
Description for robot. Use following cmd to launch robot description. (Need dummy robot or real robot for joint_states).
One robot:
ros2 launch mycobot_280pi_description one_mycobot_280pi.launch.py robot_name:=robot0 robot_xyz:='"0 0 0"' robot_rpy:='"0 0 0“’
Two robots:
ros2 launch mycobot_280pi_description two_mycobot_280pi.launch.py robot0_name:=robot0 robot0_xyz:='"0 0 0"' robot0_rpy:='"0 0 0"' robot1_name:=robot1 robot1_xyz:='"0 0.5 0"' robot1_rpy:='"0 0 0"'

## Slide 13: 감사합니다
https://www.neuromeka.com/landing
주소 서울시 성동구 연무장5가길 7 성수역 현대테라스타워 W동 15층
전화 070-4791-3103
팩스 070-4032-3327
메일 sales@neuromeka.com